## Slide 1: Adaptive Traffic Signal Control Using Multi-Agent RL
Sonu Dixit

## Slide 2: Problem Formulation
Environment = Whole traffic Network
Every junction is an Agent, working in a common environment.
Every agent can experience a part(local data) of environment.
State:
  Congestion at each incoming lane
  Congestion at immediate Neighbors incoming lanes
  Current Phase
Action : Green signal duration {20,25,30,….65,70}
Reward : Change in congestion at its lanes and neighbors lanes after performing action
Objective : Maximize discounted sum of rewards
Agent Description

## Slide 3
Data For Training:
PTV Vissim Simulation for modelling Traffic behaviour
Queue Counters for getting congestion in a lane at particular time
Self Designed Network

## Slide 4: Algorithm Used
PPO, Advantage Actor critic
Entropy Loss included as well
Buffer of 100 latest samples

## Slide 5: Algorithm
Get s,a,r,s’. put into buffer
if buffer has enough samples
3. K times:
4. Sample minibatch(32) from buffer
5. Train actor(current_policy) on this data
6. Train Critic on whole buffer
7. Set old_policy = current_policy
8. Empty buffer
Start Simulation
For every Agent that needs to take action
Both are simple Dense Network, 2 Hidden layers (64 nodes each)
PPO loss epsilon = 0.2
Entropy loss coefficient = 0.01
Two actor networks( old, new), 1 critic network for every agent
Actor Critic Network Details

## Slide 6
Traffic Network for experimentation
6 junctions, 8 signals(que_counters) per junction
10 Vehicle Input points
Left, Straight, Right = 0.25, 0.50, 0.25
1
2
3
4
6
5

## Slide 7: Experimentation and Results
1k vehicles per hour at every incoming lane
Avg Occupancy Comparison with fixed time algorithms

## Slide 8: Experimentation and Results
1k vehicles per hour at every incoming lane,
Avg Speed Comparison, calculated in 1000secs interval

## Slide 9: Experimentation and Results
1k vehicles per hour at every incoming lane,
Delay Stop Avg, calculated in 1000secs interval

## Slide 10: Experimentation and Results
2k vehicles per hour at every incoming lane
Avg Occupancy Comparison with fixed time algorithms

## Slide 11: Experimentation and Results
2k vehicles per hour at every incoming lane,
Avg Speed Comparison, calculated in 1000secs interval

## Slide 12: Experimentation and Results
2k vehicles per hour at every incoming lane,
Delay Stop Avg, calculated in 1000secs interval

## Slide 13: Experimentation and Results
3k vehicles per hour at every incoming lane
Avg Occupancy Comparison with fixed time algorithms

## Slide 14: Experimentation and Results
3k vehicles per hour at every incoming lane,
Avg Speed Comparison, calculated in 1000secs interval

## Slide 15: Experimentation and Results
3k vehicles per hour at every incoming lane
Delay Stop Avg, calculated in 1000secs interval

## Slide 16
RL Agent Performance Comparison at different vehicle incoming density

## Slide 17
RL Agent Performance Comparison at different vehicle incoming density

## Slide 18: Experimentation and Results
Random vehicle input density:
Changing after every 50 minutes
Selected in range {500,1000,………,3000,3500} vehicles per hour
Asymmetric vehicle incoming density at every junction
Avg Occupancy Comparison with fixed time algorithms
Agent was never trained in this kind of changing environment.
Still it has generalized reasonably well.

## Slide 19: Experimentation and Results
Random vehicle input density:
Changing after every 50 minutes
Selected in range {500,1000,………,3000,3500} vehicles per hour
Asymmetric vehicle incoming density at every junction
Avg Speed Comparison with fixed time algorithms
Agent was never trained in this kind of changing environment.
Still it has outperformed all fixed time algorithms.

## Slide 20: Experimentation and Results
Random vehicle input density:
Changing after every 50 minutes
Selected in range {500,1000,………,3000,3500} vehicles per hour
Asymmetric vehicle incoming density at every junction
Avg Delay Stop time Comparison with fixed time algorithms
Agent was never trained in this kind of changing environment.

## Slide 21: Phasing Analysis
For Asymmetric Network simple phasing performs better.

## Slide 22: References
Proximal Policy Optimization Algorithms (John Schulman, Filip Wolski, Prafulla Dhariwal, Alec Radford, Oleg Klimov )
Multi-agent reinforcement learning for traffic signal control, Prabuchandran K.J. , Hemanth Kumar A.N , Shalabh Bhatnagar